## Slide 1: Medical Gas Administration

## Slide 2: Oxygen Therapy
Medical gases are drugs
RTs assess need for therapy, recommend and administer dosage, determine goals of therapy, monitor response, alter therapy accordingly, and record their data in the pt record (chart)

## Slide 3: Oxygen Therapy General Goals/Objectives
  Correcting hypoxemia
    By raising alveolar and blood levels of oxygen
    Easiest objective to attain and measure
  Decreasing symptoms of hypoxemia
    Supplemental O2 can help relieve symptoms of hypoxia
      Less dyspnea/WOB
      Improve mental funx

## Slide 4: Oxygen Therapy Goals/Objectives – cont.
  Minimizing CP workload
    CP system will compensate for hypoxemia by –
      Increasing ventilation to get more O2 in the lungs and to the blood
        Increased WOB
      Increasing cardiac output to get more oxygenated blood to tissues
        Hard on the heart, especially if diseased
    Hypoxia causes Pulmonary vasoconstrix and Pulmonary HyperTxn
      These cause an increased workload on the right side of the heart
        Over time, the right heart will become more muscular and then eventually fail (Cor Pulmonale)
Supplemental O2 can relieve hypoxemia and relieve pulmonary vasoconstrix and HyperTxn by reducing right ventricular workload

## Slide 5: Oxygen Therapy
O2 % delivered
FiO2

## Slide 6: Oxygen Therapy
Assessing the need for oxygen therapy
  3 basic ways
    Laboratory measures – Invasive or noninvasive
    Clinical problem or condition
    Symptoms of hypoxemia

## Slide 7: Oxygen Therapy
Assessing the need for oxygen therapy
    Laboratory measures – Invasive or noninvasive
      PO2 – Partial pressure of oxygen
        PAO2 – Partial pressure of oxygen in alveoli
        PaO2 – Partial pressure of oxygen in arterial blood
      Hgb Saturation
        SaO2 – Arterial Saturation of Oxyhemaglobin
        SpO2 – Pulse Oximetry of Oxyhemaglobin Saturation

## Slide 8: Oxygen Therapy
Assessing the need for oxygen therapy
    Clinical problem or condition
      Specific clinical problems or conditions where hypoxemia is common
        Post-op
        COPD
        PE
        Etc.

## Slide 9: Oxygen Therapy
Assessing the need for oxygen therapy
    Symptoms of hypoxemia
  Respiratory, Cardiovascular, and Neurological
    Tachycardia, Tachypnea, hypertxn, cyanosis, dyspnea, disorientation, clubbing, etc.

## Slide 10: Oxygen Therapy – Assessing the Need for
  RT will combine objective and subjective measures to confirm inadequate oxygenation
    Often will recommend administration based solely on subjective measures

## Slide 11: Oxygen Therapy – Design & Performance
Requires expert in-depth knowledge
  What is the FiO2 range?
  Low = <35%
  Mod = 35 - 60%
  High = >60%
Does the FiO2 remain fixed or variable when pt demand changes?
  Fixed
    FiO2 does not vary
  Variable
    FiO2 varies when pt changes
  Dependent on provided flow and Pt demand

## Slide 12: Oxygen Therapy Design & Performance
  Low-flow
    Flow does not meet inspiratory demand
    O2 is diluted with air upon inspiration
    Nasal cannula
    Nasal catheter
    Tracheal catheter

## Slide 13: Nasal Cannula

## Slide 14: Oxygen Therapy Low-Flow Devices
    Nasal cannula
      Adult
        0-6 l/m
        >4L requires humidity (?)
        Can cause irritation, dryness, bleeding, etc.
        Rule of thumb for nasal
          With normal rate/depth
          [4 X (L/M)] + 20 = ~FiO2
            24-44%
      Neo
        0-2 l/m

## Slide 15: Oxygen Therapy Low-Flow Devices
    Nasal catheter
      Adult
        Visualize placement or blind to depth = to length of nose to tragus
        Replace Q8hrs
          Affects secretion, irritax, etc.
        Good for short procedures
          bronchoscopy

## Slide 16: Oxygen Therapy Low-Flow Devices
    Xtracheal catheter
      Surgically inserted in trachea
      Uses trachea/upper airway as reservoir
        Requires very low flows to meet needs

## Slide 17: Oxygen Therapy Low-Flow Devices
    Performance characteristics of low-flow
      FiO2 varies with amount of air dilution, pt-dependent
      Must assess response to therapy
      Rule of thumb nasal cannula
        With normal rate/depth
          [4 X (L/M)] + 20 = ~FiO2

## Slide 18: Oxygen Therapy Low-Flow Devices
    Troubleshooting low-flow
      Obstruction
      Displacement
      Irritation
    Reservoir Systems
      Builds O2 supply in reservoir b/w breaths
      Reduces air dilution
      Reduces O2 use, increased utilization
      Provides higher FiO2 @ lower flows

## Slide 19: Oxygen Therapy Low-Flow Devices
  Reservoir cannula
      Frequent replacement
      No humidification
      Requires nasal exhalation
    Nasal
      Stores ~20ml
      Aesthetically displeasing
    Pendant
      Better aesthetically
      Extra weight can irritate ears/face

## Slide 20: Oxygen Therapy Low-Flow Devices
Reservoir masks
  Simple mask
  Non-rebreather
  Partial non-rebreather
  Non-rebreathing reservoir circuit

## Slide 21: Low-Flow Devices Reservoir Masks
Simple mask
    Gas gathers in mask
    Exhalax ports
    Air entrained through ports and around mask
    5-10 L/M
      <5 = CO2 rebreathing
      >10 = use more invasive mask

## Slide 22: Partial rebreather, Non-rebreather

## Slide 23: Low-Flow Devices Reservoir Masks
Partial rebreather
  Utilizes 1L reservoir bag and mask
  No valves
    1st third (dead space) is breathed into reservoir bag and rebreathed
    Air entrainment from ports and around mask
  Adequate flow as long as reservoir bag does not collapse on inspiration

## Slide 24: Low-Flow Devices Reservoir Masks
Non-rebreather
  Utilizes one-way valves
    b/w reservoir and mask
    on one exhalax port
  Leak-free will provide 100%
    >~70% FiO2 is rare
      Hard to provide a leak-free system

## Slide 25: Low-Flow Devices Reservoir Masks
Non-rebreathing reservoir circuit
  Principle same as mask system
    Reservoir
      Can be a piece of blue tubing or res bag
  Can be used with Tpiece on Trach/ETT
    Utilizes failsafe inlet valve

## Slide 26: Low-Flow Devices Reservoir Masks
    Troubleshooting reservoir systems
      Irritax
      Obstrux
      Dislodgement

## Slide 27: Low- vs. High-Flow vs. Reservoir

## Slide 28: Oxygen Therapy High-Flow Devices
High-flow
  Supplies given FiO2 @ flows higher than inspiratory demand
    Peak I Flow = 3 X Minute Ventilation
    Minute Vent = f x Vt
    20L/m is upper end of normal Minute Ventilation (60L/M)
  Uses entrainment or blenders

## Slide 29: Oxygen Therapy High-Flow Devices
Principles of gas mixing –
    Find FiO2 when you know air and O2 flows
    When given an FiO2, find air – O2 ratio and total flow
    Magic box
    O2 and air flow needed for a given FiO2 and total flow

## Slide 30: Find O2 %, Air & O2 Flow Given
What is the O2 % when mixing 6L of O2 and 6L of air?
  O2 % = (Air flow x 20) + (O2 flow x 100)
        Total Flow
        = (6 x 20) + (6 x 100)
        12
        = (120) + (600)
        12
        = 60%

## Slide 31: Given FiO2, Find Ratio and Total Flow
Order to deliver 40% O2
  Air = 100 - FiO2
  O2 FiO2 - 20
  = 100 - 40
  40 - 20
  = 60 = 3 = 3 parts air
  20 1 1 part O2
  If O2 flowmeter is set at 5L/m, you are entraining 15L/m Air. Total flow = 20L/m

## Slide 32: Air 100 – FiO2 = 30 = 3 = 0.6 parts air to 1 part O2 O2 20 – FiO2 50 5 1
If O2 flowmeter is set at 6L/m
air entrained = 3.6L/m, O2 flow = 6L/m
total flow = 9.6 L/m

## Slide 33: Given FiO2 and Total Flow, Find Flow to Set your O2 Flowmeter to
FiO2 ordered = .35 Total flow = 60L/m
O2 Flow = (total flow) (FiO2 - 20)
79
= (60 l/m) (35 - 20)
79
set O2 flowmeter = 11.4 l/m

## Slide 34: Oxygen Therapy High-Flow Devices
Air entrainment system
  Amount of air entrained varies directly with port size and velocity
  The more air entrained,
    Higher flow
    Lower FiO2

## Slide 35: Oxygen Therapy High-Flow Devices – Entrainment
FiO2 depends on
  Air to O2 ratio (Amount of air entrained)
  Downstream resistance (Backpressure)
    Increased resistance
      Decreases entrainment
        Decreases total flow
        Increased FiO2
    % O2 delivered may increase, but FiO2 may decrease due to insufficient flow for insp demand

## Slide 36: Oxygen Therapy High-Flow Devices – Entrainment
Input flow changes
  Nominal effect on FiO2
  Changes total flow
Magic box
  Only for estimax
  For accuracy use E38 - 2

## Slide 37: Oxygen Therapy High-Flow Devices – Entrainment
AE devices
  AEM (Venti-mask)
  AE Nebulizer (Large volume nebulizer)
    Cool/heated aerosol

## Slide 38: Oxygen Therapy High-Flow Devices – Entrainment
  Air entrainment mask
    Adjustable air entrainment ports and jets to precisely control FiO2 and flow
    The higher the flow, the lower the FiO2
      (Inverse relaxship) vice versa
    For precise FiO2’s, total flow must be >Insp demand (Peak Insp flow) (3 X min vent)
    Aerosol collar
      Allows connection of a humidified gas to the entrainment port

## Slide 39
AEM

## Slide 40: Oxygen Therapy High-Flow Devices – Entrainment
  Air entrainment nebulizer (Cool/heated aerosol mask)
    Same as mask, except
      There is additional temp and humidity control
        It allows for administrax of particulate water (sterile) to airway
          Great for trachs (Heated)
          Airway edema (Cool)
      It has fixed jets; port is only variable
        Limits O2 flow to 12-15 l/m
      Provides fixed FiO2 only when total flow exceeds insp demand
        Face tents provide less-consistent FiO2

## Slide 41: Oxygen Therapy High-Flow Devices – Entrainment
LVN contd.
  Determining if total flow is sufficient
    Visual inspex
      Aerosol mist is seen exiting tubing on insp and flow is constant
      Pt Vt compared to neb flow

## Slide 42: Oxygen Therapy High-Flow Devices – Entrainment
Troubleshooting air entrainment systems
  Affected by downstream resistance
    Water in tubing
    Obstruction

## Slide 43: Oxygen Therapy High-Flow Devices – Entrainment
  Providing moderate to high FiO2 @ high flow
    @100% a LVN can only provide 12-15L/M
    To be a true high-flow device, it must ensure constant FiO2 by providing full insp demand

## Slide 44: Oxygen Therapy High-Flow Devices – Entrainment
  Providing moderate to high FiO2 @ high flow
  Methods
    Add reservoir tubing if intubated or trached
    Closed reservoir
      3-5L anesthesia bag w/ emerg inlet valve
    Shotgun
      Dual LVNs
      Most common
    Lower entrainment
      Decrease FiO2, increase flow
      Add supplemental O2 to mask

## Slide 45: Dual Nebulization System

## Slide 46: Oxygen Therapy High-Flow Devices – Entrainment
Problems w/ downstream flow resistance
  Downstream pressure from the entrainment port
    Increases back P
    Decreases entrainment
      Increases FiO2
      Decreases flow
    Results in variably delivered FiO2
      Not enough flow to meet insp demand

## Slide 47: Oxygen Therapy More Reservoirs
Enclosures
  Tents
  Hoods
  Incubators
Others
  BVM
  Pulse dose cannula
  Concentrators

## Slide 48: Oxygen Therapy More Reservoirs – Enclosures
    Hoods
      Best method to deliver controlled O2 to infants
      Covers only head
        Ideal to allow nursing access
      7 L/m minimum flow
        To flush adequately
      Flows above 10 - 15 L/M are contraindicated
        Generates damaging noises, cold and dry
        Cold stress can increase O2 consumpx and apnea
      Analyze FiO2 @ pt head level (layering)
      Must heat and humidify incoming gas
        Do not direct at pt face
        Maintain neutral thermal environment
          Age and weight appropriate

## Slide 49: Oxygen Therapy More Reservoirs – Enclosures
Incubator (Isolette)
  Plexiglas enclosure
  Servo-controlled convex heating with supplemental O2
  Freq opening and dilution make it hard to deliver high O2
  Hoods are used in incubators to provide supplemental O2

## Slide 50: Oxygen Therapy More Reservoirs – Others
Others
  BVM
    Resuscitation bag
  Pulse dose cannulas
  Oxygen concentrators

## Slide 51: Oxygen Therapy High-Flow Devices – Blenders
Blending systems
  Used when entrainment cannot provide high enough FiO2 @ high flows
  Need frequent analyzing for safety
  Methods
    Manual mixers
    Blenders

## Slide 52: Oxygen Blender

## Slide 53: Oxygen Therapy High-Flow Devices – Blenders
  Blending methods
    Mixing gas manually
      Individual air and O2 flow meters combined for a desired FiO2 and flow
    Oxygen blenders F38 - 20
      Air and O2 inlets
      P regulated
      Precision-blended for FiO2 and flow
      Alarms for O2 delivery outside of set range
      Prone to inaccuracy and failure

## Slide 54: To Calculate FiO2 Blending Two Devices
(FiO2)(V total)+ (FiO2)(V total) =FiO2
V total + V total
(.7)(20)+(.5)(20) = FiO2
20 + 20
14 + 10 =24 = .6
40 40

## Slide 55: Oxygen Therapy Selecting Delivery Approach
Not one best method every time
The RT and their expert knowledge need to be available for –
  Consultation
  Assessment/reassessment
  Alterax of therapy
  Discontinuax of therapy

## Slide 56: Oxygen Therapy Selecting Delivery Approach
  Purpose (Objective)
    Increase FiO2 to correct hypoxemia
    Minimize symptoms of hypoxemia
    Minimize CP workload
  Patient
    Cause and severity of hypoxemia
    Age
    Neuro status/orientax
    Airway in place/protected
    Regular rate and rhythm (Minute Ventilax)

## Slide 57: Oxygen Therapy Selecting Delivery Approach
Equipment performance
  The more critical, the greater need for high, stable FiO2
    Becomes more difficult the more critical the situation, due to pt varying pattern

## Slide 58: Oxygen Therapy Selecting Delivery Approach
  Pt categories
    Emergency
      Highest FiO2 possible
      Highest PaO2 possible
    Critical adult
      >60% O2
      PaO2 >60mmHg
      SpO2 >90%
    Stable adult, acute illness, mild hypoxemia
      Low to mod FiO2
      Response to therapy, not precise concentraxs

## Slide 59: Oxygen Therapy Selecting Delivery Approach
Pt categories cont.
    Chronic dx adult, acute on chronic illness
      Ensure adequate oxygenax without depressing ventilation
        SpO2 85 - 90%
        PaO2 50 - 60mmHg
        Use venti mask to control FiO2 precision
        Assess response to therapy!
        If not maintainable on cannula, use masks
          Pt may remove mask frequently due to
            Discomfort
            Convenience
            Change in mental status
          Encourage cannula use b/w mask use if mask must come off for periods

## Slide 60: Oxygen Therapy
Protocol-based O2 therapy
  Will ensure
    Initial assessment
    Qualifying measure for protocol
    Modifiable tx plan according to need
    Discontinuation of therapy per protocol

## Slide 61: Oxygen Therapy Precautions & Hazards
  O2 toxicity
    Primarily affects lungs and CNS
    2 determining factors of O2 tox
      PO2
      Time of exposure
      I.e. the higher the PO2 and exposure time, the greater the toxicity
    CNS effects occur with hyperbaric pressures
    Pulmonary effects can occur @ clinical PO2 levels
      Patchy infiltrates on x-ray, prominent in lower lung fields
      Major alveolar injury

## Slide 62: Oxygen Therapy Precautions & Hazards
O2 toxicity cont.
    Pathophysiology
      High PO2 damages capillary endothelium
      Followed by interstitial edema and AC membrane thickening
      Type I cells are destroyed (Cells that create new lung tissue, gas xchange cells)
      Type II cells proliferate (trigger inflamax response)

## Slide 63: Oxygen Therapy Precautions & Hazards
O2 toxicity cont.
    Pathophysiology cont.
      Exudative phase
        Alveolar fluid buildup (from inflamax response) leads to
          Low ventilation/perfusion ratio (shunting)
          Hypoxemia
          Hyaline membranes form @ alveolar level
            Proteinaceous eosinophilic (basic) material
            Composed of cellular debris and condensed plasma proteins
          Pulmonary fibrosis develops
          Pulmonary HyperTxn develops

## Slide 64: Oxygen Therapy Precautions & Hazards
O2 toxicity cont.
    Cause
      Overproducx of O2-free radicals
        Byproducts of cellular metabolism
        Toxic in excessive amounts
        Normally, antioxidants and other special enzymes dispose of excess free radicals
        Neutrophils (WBCs) and macrophages flood the infiltrate the tissue and mediate inflammation response, leading to more free radicals

## Slide 65: Oxygen Therapy Precautions & Hazards
O2 toxicity cont.
    How much is too much?
      >50% for very extended times
      >PO2 the less time it takes
    Goal
      Use the lowest FiO2 possible to maintain adequate tissue oxygenation
    Other consideraxs
      Growing lungs are more sensitive to O2
        Retinopathy of Prematurity (ROP)
        Bronchopulmonary Dysplasia (BPD), chronic lung dz
      Never withhold O2 from a hypoxic pt
        Alternative is death due to tissue hypoxia

## Slide 66: Oxygen Therapy Precautions & Hazards
  Depression of ventilation
    Hypercarbic drive is blunted
      High PCO2 no longer stimulates pt to increase ventilation
    Suppression of hypoxic drive

## Slide 67: Oxygen Therapy Precautions & Hazards
Depression of ventilation – cont.
      The only stimulus left to increase ventilation is due to hypoxia
      When you add too much O2, (remove the hypoxia), you effectively remove the neurological stimulus to breathe (peripheral chemoreceptors)
        Hypoventilation occurs
          VDS/VT ratio increases
      CO2 continues to elevate to sedative levels
        Pt stops breathing until hypoxic again
        If CO2 is too high, they will remain sedated and code (CP arrest)
      Never withhold O2 therapy from a hypoxic pt (PaO2)
      True hypoxic drive is extremely rare

## Slide 68: Oxygen Therapy Precautions & Hazards
  Retinopathy of Prematurity (ROP) retrolental fibroplasia
    Up to 1 month of age
    Excessive blood oxygen level causes retinal vasoconstrix
    Leads to necrosis of the vessels
    New vessels proliferate
      These new and fragile vessels hemorrhage and cause scarring
      Scarring leads to retinal detachment and blindness
    Keep PaO2 <80mmHg (American Academy of Pediatrics)

## Slide 69: Oxygen Therapy Precautions & Hazards
  Absorption atelectasis
    Normal alveoli content is room air
    O2 and CO2 diffuse and replace each other as they load and unload the lungs and blood
    If high levels of O2 are used
      No “non-diffusing” gases remain in the lung
      The O2 will diffuse, leaving the alveoli nearly vacant and collapsing it
    Can also occur with hypopnea/hypoventilax patterns
      Sedax, surgical pain, CNS dysfuncx, etc.

## Slide 70: Oxygen Therapy Precautions & Hazards
Absorption atelectasis – cont.
    Can be used to remove free air from body cavities
      After removing normal levels of “non-diffusing” gases from the lungs, the blood quickly depletes its level of these gases and will absorb them from the free air in the cavities it is residing in

## Slide 71: Oxygen Therapy Precautions & Hazards
  Fire
    Fire triangle
      O2, heat, and fuel
    Increase risk of fire
      High concentration of O2
      High pressures of O2
    Reduce O2 buildup in enclosed environments
      Under drapes
      Operating rooms, etc.
    Be cautious when using electronic equipment
      Scalpels, cardioversion, cardio shock